## Slide 1: Introduction to Switches

## Slide 2: Switch Access
Switches are simple buttons that can be pressed to access a communication aid.
Just one button provides complete access to all symbols and device functions through a system known as scanning.

## Slide 3: How does the Switch Work?
Works in a similar manner to Partner Assisted Scanning .
The computer scans through each symbol on screen, one at a time.
This can usually be seen with a visual highlight, but some people also have the symbol read aloud to help.
When the desired symbol is highlighted by the computer, the user hits the switch to select it.

## Slide 4: Types of Switch
There are a lot of switches available. The vary mostly on the part of the body used to press the switch, and the movement of that body part.
This image shows a red specs switch which the user accesses by moving his head to the right.

## Slide 5: Types of switch
The girl In this photograph is using a buddy button with her hand.
The buddy button is also suitable for positioning on a wheel chair by a knee or an elbow.
It can also work by foot.

## Slide 6: Types of Switch
The wobble switch is useful for children who use large arm movements to press the switch.
The whole top column of the switch ‘wobbles’ in any direction when hit.
The large surface area is difficult to miss!

## Slide 7: Types of Switch
The Sip & Puff switch is suitable to people with good breath control and who find it difficult to use other switches.
The switch is actually two switches (one for sipping and one for puffing).
Children with tracheotomies can still use sip and puff switches if they can control their cheek muscles.

## Slide 8: Simple scanning
In simple scanning the computer highlights one symbol at a time. The child presses their switch when the symbol they want is highlighted. It usually takes 1-5 seconds to pause at each symbol. Timing skills and reliable movements are critical!

## Slide 9: Simple scanning
In simple scanning the computer highlights one symbol at a time. The child presses their switch when the symbol they want is highlighted. It usually takes 1-5 seconds to pause at each symbol. Timing skills and reliable movements are critical!

## Slide 10: Simple scanning
In simple scanning the computer highlights one symbol at a time. The child presses their switch when the symbol they want is highlighted. It usually takes 1-5 seconds to pause at each symbol. Timing skills and reliable movements are critical!

## Slide 11: Simple scanning
In simple scanning the computer highlights one symbol at a time. The child presses their switch when the symbol they want is highlighted. It usually takes 1-5 seconds to pause at each symbol. Timing skills and reliable movements are critical!

## Slide 12: Simple scanning
In simple scanning the computer highlights one symbol at a time. The child presses their switch when the symbol they want is highlighted. It usually takes 1-5 seconds to pause at each symbol. Timing skills and reliable movements are critical!

## Slide 13: Simple scanning
In simple scanning the computer highlights one symbol at a time. The child presses their switch when the symbol they want is highlighted. It usually takes 1-5 seconds to pause at each symbol. Timing skills and reliable movements are critical!

## Slide 14: Simple scanning
In simple scanning the computer highlights one symbol at a time. The child presses their switch when the symbol they want is highlighted. It usually takes 1-5 seconds to pause at each symbol. Timing skills and reliable movements are critical!

## Slide 15: Simple scanning
In simple scanning the computer highlights one symbol at a time. The child presses their switch when the symbol they want is highlighted. It usually takes 1-5 seconds to pause at each symbol. Timing skills and reliable movements are critical!

## Slide 16: Actvity
Imagine a young girl with cerebral palsy. It takes her 3 seconds to reliably make the movement required to press the switch.
We need to pause on each symbol long enough for her to be able to make this movement, so we allow 4 seconds.
In the previous group of symbols how long would it take to get to the mouse?

## Slide 17: Making Scanning Faster
Scanning is usually slow compared to the other access options. However, there are ways to make it much faster, such as ensuring that the symbols are laid out on the screen so the most often used require less time and switch presses to get to them.
Whole row and column scanning is often used to reduce the time to get to
Symbols can also be grouped, and so the groups are scanned before the symbols within each group.

## Slide 18: Row/Column Scanning
Row and column scanning is much more efficient compared to stepping through each symbol one at a time. For single switch users it requires two presses instead of one (one for the row and then the second for the symbol).

## Slide 19: Row/Column Scanning
Row and column scanning is much more efficient compared to stepping through each symbol one at a time. For single switch users it requires two presses instead of one (one for the row and then the second for the symbol).

## Slide 20: Row/Column Scanning
Row and column scanning is much more efficient compared to stepping through each symbol one at a time. For single switch users it requires two presses instead of one (one for the row and then the second for the symbol).

## Slide 21: Row/Column Scanning
Row and column scanning is much more efficient compared to stepping through each symbol one at a time. For single switch users it requires two presses instead of one (one for the row and then the second for the symbol).

## Slide 22: Elimation Scanning
Elimination switch access removes the standard scanning element altogether and instead uses non-linear switch presses to navigate to the desired symbol.
It does this by dividing the symbols into two groups and then subdividing the group when the appropriate switch is pressed.
This is a feature in the Grid 3 software

## Slide 23: Elimination Scanning
Elimination scanning divides the collections of symbols on the page into at least two colours. Each colour represents a switch (so you need to use at least two switches for this to work). To select the owl we simply press the switch that corresponds to the colour behind the owl (blue!)

## Slide 24: Elimination Scanning
Now the blue half has been subdivided into two new halves, again using the same two colours which represent the two switches. The owl is still in the blue area so we press the blue switch again.

## Slide 25: Elimination Scanning
Press the blue switch again…

## Slide 26: Elimination Scanning
This time the owl is highlighted with the orange colour, so we must his the switch that corresponds to orange this time.

## Slide 27: Elimination Scanning
Another blue…

## Slide 28: Elimination Scanning
And finally orange will select the owl. This selection took six switch presses to get to the owl.

## Slide 29: Activity
Consider the elimination scan and the standard scanning.
Why might you choose one over another for a child that you are working with?
Notes: Suggested that you use the popcorn approach again.

## Slide 30: The Importance of Positioning
0.7 cm
The Microlight is a very useful switch for people with very little movement, requiring just 0.7cm of movement to activate the switch.
Often the microlight is positioned on its side, so a little movement in the tip of a finger resting on a desk is enough to operate it.
But here there is no tolerance for error! The switch must be placed very accurately in order for it to work.
How do we position such switches? Velcro!

## Slide 31: Velcro & Dycem
Maxess trays are Velcro boards that come in a range of sizes to fit wheelchair trays.
You can also stick Velcro directly onto wheelchair trays or tables.
Dycem also stops switches from moving around, but is not a strong as Velcro and works best with heavier switches.

## Slide 32: Positioning Switches
It’s almost always preferable to use the hands to access the switches if possible. Think about where you would place a switch for children who are able to consistently make the following movements:
extend elbow to move forearm (like banging a drum)
move forearm at elbow (like using a pencil eraser)
rotate hand (from palm down to palm up)
make a hand wave
make a door knocking movement
make a pointy finger or stick thumb out

## Slide 33: Positioning Switches
If you can’t find a reliable hand or arm position then have a think about the head and legs. Think again about where you would place a switch for these movements:
nodding head
rotating head (like a ‘no’ movement)
tipping head from side to side
pushing knees out to the sides (and bringing them back!)
tapping a foot

## Slide 34: Positioning Switches
Just because someone can hit a switch doesn’t mean it’s in the best position! You need to consider aspects such as:
How much effort is required to hit the switch?
Can they hit it in a timely manner?
Does it cause their pelvis to move?
Does it result in lots of other unwanted movements?
Does the child like the position of the switch?
Is it practical to mount the switch in the position you’ve chosen?

## Slide 35: Helping choose a switch position
Affective Communication analysis
Complexneeds.org.uk
ACA Observation Sheet

## Slide 36: Mounting Switches
Switches are often mounted to headrests for head control, to the wheelchair seat for knee control, and to the foot rests for foot control.
The L3D mounts from Rehadapt allow switches to be positioned very accurately
The Meru Flexi mount allows for changes in position as the switch can be moved without tools

## Slide 37: Stephen Hawking
Hawking used a small infrared switch carefully positioned on a mount on his glasses.
The tolerance for the position of this switch is tiny, but Hawking had staff with him who were trained to reposition it when necessary.

## Slide 38: Switch Selection Tool
You can download this tool to help guide you through Selcxting and using a switch for access and AAC
Start Switch Guide

## Slide 39: Switch Progression
The more accurate and confident a child becomes in using a switch the greater the range of options they have to use that switch in different ways.
Communication and Control are two of the most popular.
SENswitcher demonstrates clearly a switch progression for use in different settings
It is based on switch control skills
SENswitcher
This can also be downloaded from Global Symbols

## Slide 40: Connecting a Switch to a device
Connecting a switch to any sort of a device requires an interface
The connection can be physical with a cable and interface box
Or it can be wireless such as Bluetooth
There are many options for connecting a switch to a computer
How do we connect a switch to our Tablet

## Slide 41: Connecting a Switch to a device
Switch
Interface Box
Tablet
Bluetooth Enabled Switch
Bluetooth Connection
Paired Tablet

## Slide 42: Switch Games
Making using a switch fun is important
Give the child something that is motivating to practice accoueacy and timing
This can be fun for families
http://oneswitch.org.uk/is a great resource for free switch games for PC’s
Here are some great examples for older computers
Start LightBox for windows
Start Star Wars
Start Whack a Mole